## Slide 1: Performance, Reliability and Maintenance of the SNS Superconducting Linac and its upgrade
Presented at
Accelerator Seminar, Jefferson Lab.
June 18, 2020
Sang-ho Kim
Spallation Neutron Source
Oak Ridge National Lab.

## Slide 2: Outline
SNS and SNS SCL overview
SNS operational statistics
SCL performance and maintenance
Proton Power Upgrade (PPU) Project
Summary

## Slide 3: SNS and SNS SCL overview

## Slide 4: SNS machine layout
H- stripped to p
2.5
DTL
86.8
CCL
402.5 MHz
805 MHz
SRF, b=0.61
SRF, b=0.81
186
387
1000 MeV
Linac; 1 GeV acceleration
Front-End: Produce
a 1-ms long, chopped, H-beam at 60 Hz
upgrade
945 ns
1 ms macro-pulse
Average macro-pulse beam current: 26 mA
Current
mini-pulse
Chopper system makes gaps
Ring: Accumulate 1-ms long pulse to 700 ns
Liquid Hg Target
Current
1 ms
259 m
157 m
71 m

## Slide 5: SNS superconducting linac
The first SRF technology for large scale pulsed proton machine
Designed for H- beam acceleration from 186 MeV to 1000 MeV
Two types of cavity geometries to cover board range of particle velocities
  33 medium beta (βg=0.61) SRF cavities
  48 high beta (βg=0.81) SRF cavities
157-m long, 81 independently powered 805-MHz SRF cavities in 23 cryomodules
71-m long space is reserved for energy upgrade

## Slide 6: SNS cryomodule design basis
Cryomodule: similar construction arrangement employed in CEBAF (space frame, end-cans, etc.)
Cryogenics
  Heat exchanger for primary in return end-can
  FPC outer conductor cooled by 5-K supercritical helium
Fundamental power coupler (FPC): scaled from KEK 508-MHz coupler
HOM coupler: scaled from TTF HOM coupler in case of large HOM induced power
Mechanical tuner: adapted from Saclay-TTF design
Piezo tuner: adapted later. Integrated into one of tuner mounting legs in case of unexpected large LFD
End-group material: Reactor grade niobium

## Slide 7: SNS Operation and operational statistics

## Slide 8: SNS operation schedule
Planned neutron production hours in recent years: 4,700~4,900 (green)
  Input from ‘target management plan’ and major maintenance activities
  Goal in near future: 5,000 planned hours at > 90% availability

## Slide 9: Beam power on target since FY07
Various issues has been encountered and addressed
SNS has achieved a stable operation at 1.4 MW

## Slide 10: Overall machine performance in FY20
Operational reliability remains excellent
  Overall machine availability for neutron production in FY20 to date: 95%
Beam Power on Target (kW)
Integrated beam power per day (MWh)

## Slide 11: SCL Reliability
Availability last 10 years:
  Whole SCL system including CHL, RF, HVCM, Control, Vacuum, etc.: 98.1 %
  SRF cavities/cryomodules: 99.6%
    Average trip or downtime: <1 trip/day corresponding to <5 min./day
Sustainability for the future and cavity performance improvement
  In-situ and/or offline repairs
  Developed spare cryomodules
  Deployment of in-situ plasma processing
Up to 6/9
Availability (%)

## Slide 12: SCL performance and maintenance

## Slide 13: SNS SCL output energy at 60-pps operation evolved from 850 MeV
60-pps operation since 2008
SCL ready for 1.4 MW in 2011
First neutron production at 1.4 MW in June 2014
SCL output energy at 1 GeV since May 2018
Routine 1.4-MW operation since 2018
Linac output energy (MeV)
850 MeV
1 GeV

## Slide 14
Linac output energy (MeV)
Performance improvement
by novel in-situ plasma processing
Spare HB cryomodule
development
Cryomodule rework
Early stage learning,
Cryomodule part repairs,
Supporting systems improvement, and overall system optimization
Errant beam

## Slide 15: The first 1.5 years operation
Most of sub-systems were not commissioned for the operation at full duty factor
  System learning at low repetition rate, short beam pulse and low beam current
5 Hz
15 Hz
30 Hz
30 Hz
30 Hz
60 Hz demo
890 MeV
890 MeV
890 MeV
850 MeV
500 µs
18mA
18mA
375 µs
20mA
500 µs
25mA
1-GeV demo run
at 15 pps

## Slide 16: Early stage of operation
Performance of SRF cavities at < 20 pps was above design:
  75 cavities out of 81 was used for the 1-GeV demo at 15 pps.
Some subsystems at the SNS were designed to be substantial improvements compared to existing accelerators while other subsystems were first of a kind.
  Some performance and reliability aspects required a learning curve, and it took time to understand the systems as a whole and to determine the need for additional performance improvements.
Superconducting linac output energy was 850 MeV for early 60-pps operation
  Reduced operating Eacc due to thermal instability at 60-pps by electron activities
  Eacc of a dozen of cavities was limited by available RF power due to lower operating voltage of high voltage converter modulator (HVCM)
    In 2009 one additional HVCM was installed to relieve loads on HVCMs and increase the HVCM voltages
  One or two cryomodules were out of service for repair
  Addressed issues with sub-components and control/LLRF systems
Achieved 930 MeV at ~90% of the design duty factor in 2009

## Slide 17: Errant beam
In 2009, ‘Errant beam’ was first recognized.
‘Errant beam’ is an off-energy beam created
  Mostly by upstream warm linac RF cavity faults or oddly shaped beam pulse from ion source
  Beam lost in SCL till beam abortion by MPS system
Errant beam hitting SRF cavity surface desorbs gas:
  Can create discharge condition and lead to performance degradation
SNS MPS speed requirement was originally set to avoid copper damage against off-normal condition

## Slide 18: Reduction of errant beam events and duration
Severity depends on location where the beam is lost, on frequency of events and on duration of errant beam
  Frequency of events is associated with warm linac and ion source conditions. More careful conditioning and vacuum system improvement helped
  Duration of errant beam
    New dedicated MPS monitors the loss of beam current
    MPS response time shortened to ~7 μs

## Slide 19: Cavity performance recovery, cryomodule repair and spare cryomodule
Recovery of cavity performance to previously attained operating gradients
  RF conditioning and/or thermal cycling: successful so far
Cryomodule repair activities critical to sustain cryomodule performance and reliability
  Rework (in-situ or off-line) is necessary for unrecoverable damage
Spare cryomodule development in-house
  High beta spare: installed in the tunnel in Aug. 2012
  Medium beta spare: installed in the tunnel in Feb. 2020
  Both are one of highest performing cryomodules
  Allows offline repair of high beta cryomodules
  Prototype for PPU cryomodule

## Slide 20: Offline repair rework since 2009
Seven cryomodules have been removed from the tunnel for repairs since
  One due to HOM coupler
  One due to large leak in helium line in end can
  One replaced with high beta spare cryomodule
    Low performer (large x-rays). Used for first plasma processing offline
  Four due to leaks at fundamental power couplers (FPCs)
FPC leaks so far were not catastrophic
  Leak rate: high 10-7 or low 10-6 torr l/s scale leak
  turn off and wait until the next outage
Two medium beat cryomodules waiting on offline repairs
  5a: arcing around FPC but no leak
  11b: HOM coupler (never operated at SNS)

## Slide 21: Other cryomodule repairs since FY07
Instruments (PT, CCG, TC, TD): >100
JT valve actuator: ~20
Thermal cycling to remove gaseous contamination: ~12
Tuner repair: >20
  Mostly between FY06 and FY13. Only one in 2018 since FY14.
  Tuner controller failures become more frequent recently (1~2 per year)
Insulating vacuum repair/upgrade: 10 CMs require active pumping
RF component (water condensation at coupler air side, loosen connectors in CM): 3
HOM couplers: removed feedthroughs from 7 CMs

## Slide 22: Plasma processing
From 2009 to 2015, linac output energy for the stable neutron production was 925-940 MeV
  Eacc of each cavity was set based on collective limits at 60 pps.
SNS looked for cost-effective method to decrease electron activities and thus to increase Eacc
  In 2009, during attempt for helium processing for SNS cryomodule, observed RF glow discharge with very low RF power. Large reduction of field emission was measured.
  In-situ plasma processing was identified as an important area of R&D
R&D started in 2012

## Slide 23: In-situ Plasma Processing R&D
R&D started in 2012 to develop a reliable technique for in-situ plasma processing for high beta cavities
  Focused on removal of residual contamination using low density reactive oxygen plasma to decrease electron activities (Field emission and multipacting)
Successful recipe development for high beta cavities

## Slide 24: Plasma boosts to 1 GeV
8 high-beta cryomodules successfully plasma processed
  1 cryomodule offline
  7 cryomodules in the tunnel
  Accelerating gradient increased by 20% on average
  Improvement of Eacc ranges from 0 to 6.5 MV/m
  No performance degradation from plasma processing observed
Also plasma processing is ready for medium beta cavities
  Will be deployed to offline medium beta cryomodule after repair

## Slide 25: Summary of SNS SCL history
Linac output energy (MeV)
972 MeV
990 MeV
RF/Control improvement
Two CM Repairs
Other misc.
Additional
HVCM
Recognized
Errant
Beam
3 cavities
Turned off
(errant beam)
1. Full pulse length
for 1.4 MW
CMs out
from slot 6 and 20
for repair
High beta
spare CM in
for slot 20
MB CM in
(slot 6)
after repair
2. Worst performing
HB CM out (slot 19),
HB CM from slot 20 in
after repair
First in-situ
plasma
Processing (CM19)
&
Performance recoveries of degraded cavities (thermal cycling, RF conditioning)
Second in-situ
plasma
processing
CM18
Fourth in-situ plasma processing CM21, 22 & 23
1010 MeV with
increased
energy margin
939 MeV
Third in-situ
plasma
processing
CM16 & 17
1
2
957 MeV
MB Spare CM in
Linac output energy (MeV)
928 MeV
925 MeV

## Slide 26: CHL Reliability
Availability: 99.8% last ten-year average
Sustainability for the future
  Active preventative maintenances
  Developed CHL spare carbon bed
  Plan for replacing CHL helium purifier
  Plan for new 2K cold box
Several people has been qualified for CHL operation including 2-K pump-down
  Qualification program for technicians in place
  Continue to develop procedures for operation and maintenances
Availability (%)

## Slide 27: Previous issues in CHL
VFD fault and 2K cold-box trip
  Had nuisance trips (during operation and during pump-down to 2K) and became more frequent.
  Root cause was the sinus filter* for CC3 wired incorrectly from day one
  *sinus filter: LC filter between VFD and transformer for cold compressor motor
  Since this fix, no nuisance trips
2K cold-box trip due to loss of power to Mag bearing cabinet for CC4
  Root cause was a failed DC filtering capacitor
  Resulted in 22-hours down time to verify whether cold compressor was safely shut down or not
  Additional preventive actions were implemented to ensure magnetic bearing levitation and soft-landing using back-up battery power at loss of power
  So far, we believe that there has been no hard-landing of cold compressors

## Slide 28: Proton Power Upgrade (PPU) Project

## Slide 29: Proton Power Upgrade project
Accelerator capability from 1.4 MW to 2.8 MW
  Beam energy increase by 30%
  Beam current increase by 50%
2-MW First Target Station
upgrade
Existing linac
7 new
cryomodules
HPRF
HVCM
LLRF
Gallery extension
2-MW target
Ring injection
& extraction
upgrade

## Slide 30: SCL setup for 1.3 GeV for 2.8 MW
1.3 GeV is a built-in energy limit due to Lorentz stripping in HEBT
No upgrade or replacement for existing cold linac
Accelerating gradient for PPU cavities: 16 MV/m, and seven new cryomodules
1.3 GeV and 2.8 MW
1.0 GeV and 1.4 MW
Required RF power
RF power margin
Comparison of accelerating gradients
Required RF power and RF margin
for 1.3 GeV and 2.8 MW

## Slide 31: PPU cavity/cryomodule design specifications
Lessons learned are incorporated into the design
Parameters | Original SNS high-beta cryomodule design | PPU high-beta cryomodule | Demonstration of Performance
Eacc (MV/m) | 15.8 (14.8*) | 16.0 | Demonstrated with spare HB CM in operation since 2012
FPC rating. Peak, Average (kW) | 550, 50 | 700, 65 | Demonstrated with FPC qualification on test stand
Q0 | > 5 × 109 at 2.1 K | > 5 × 109 at 2.1 K | No change
External Q of FPC, Qex | 7 × 105 (±20%), fixed type | 8 × 105 (±20%), fixed type | Verified on test bench
Material of cavity | RRR>250 for cells, RRR~70 for end groups | RRR>250 for both cells and end groups | Developed 3 new medium beta cavities with RRR>300
Higher-order mode coupler | Two (one at each end group) | None | Demonstrated through HOM measurement and operation
Tuner | One mechanical tune, one fast piezo tuner | 1 mechanical tuner (no fast piezo tuner) | Demonstrated through operation
Pressure vessel | Good engineering practice | Code stamp required | Developed spare HB CM
* Average HB cavities in operation as of Sept. 2018

## Slide 32: Summary
SNS has conducted a multi-faceted approach for 1.4-MW operation at 1 GeV while keeping the machine highly reliable
Significant testing and operational experience has led to a better understanding of systems
  There will be always machine-specific issues and nuisances especially in ‘first of a kind’ machine:
    keep design simple, keep enough margin, keep room for upgrade
Lessons learned for reliable operation and high performance
  Operational flexibility is one of the critical aspects for high availability of SNS SCL
    Run with adequate energy margin to shorten downtime
  Balanced performance between all sub-systems, lead to the most reliable and efficient system
    Weakest-link limits overall performance